## Slide 1
Vanessa Gabel1, 2 and Greg Tucker1, 2
1Cooperative Institute for Research in Environmental Sciences
2Department of Geological Sciences, University of Colorado, Boulder
Rivers & Rocks
Integrating Channel Adjustments, Gravel Attrition, and Bedrock Wear in a Model of Long-Profile Evolution
12 Dec 2022

## Slide 2
Big take-away:
Upstream lithology affects downstream sediment load and erosion rates!
Observations & theory
Model development
Model behavior
Future applications

## Slide 3
Bedrock Channels
Alluvial Channels
Mixed Channels
Width is confined
Concave-up profile scales with rock properties and discharge
Abrasion is parabolic
Width is self-adjusted
Graded transport slope
Downstream fining via selective transport and attrition
Channel width is self-adjusted within fixed-width valley
Slope adjusted to both rock incision and sediment transport
Mill Creek, The Science of Rivers
Giba River, Wikipedia
South Yuba River, Daniel Nylen

## Slide 4: Where do we see mixed rivers?
Lots of places! Esp interesting over large spatial scales, lots of bedrock heterogeneity

## Slide 5
Our model builds upon previous efforts to capture the complexity of mixed bedrock-alluvial systems
Channel adjusts to flow and sediment characteristics
Bedrock is abraded by mobile sediment
Bedrock is plucked via stream power
Sediment cover modulates transport and erosion
Sediment transport adheres to equilibrium channel theory
Loss of bedload via grain attrition
Notes: Bedload sediment transport in equilibrium channels
Channel width adjustment to flow and sediment characteristics
Abrasion of bedrock by mobile sediment
Plucking of sediment
Sediment cover effects
Loss of gravel-sized sediment via grain attrition

## Slide 6
Compare to SP
Maybe compare to other ED models
Steepness uplift
Width and depth (plot on Phillips 2022)
Concavity with sed hardness
Our model reproduces expected fluvial behavior…
Notes: Show single lithology cases both for these plots and analytical solutions (if shown at all) – save this two lith stuff for last slide (future applications)

## Slide 7
…while also adding nuance to bedrock-sediment interactions

## Slide 8: Future applications ben’s 2d version exploring external forcing channel response to landsliding erosion in lith. Het. environment

## Slide 9
In Summary
Important stuff we learned

## Slide 10
Questions?

## Slide 11
midnightblue
peru
dodgerblue
goldenrod
lightgrey
darkgreen
Sienna seashell
silver

## Slide 12: Observations
Endmember paradigm – bedrock rivers and alluvial rivers
Complex landscapes have spectrum
Evolving understanding of these behaviors
Need model that moves in the direction of capturing this complexity!